## Slide 1: USB Gain/Phase Analyzer
Interim Report

## Slide 2: USB Gain/Phase Analyzer
Requirements
Design
Prototyping
Schedule
Budget
Next Steps

## Slide 3: Purpose
Test the frequency behavior of filters, amplifiers
Generate Bode plot with
amplitude and phase

## Slide 4: Requirements
Displays Bode plot on a PC
Frequency Range: 1 kHz to 150 MHz
Amplitude up to 1.25 V RMS
Phase response
Detect signals down to 60 dB below input

## Slide 5: Design — Software
PC software
  User software sends commands to the GPA
  Received data is plotted using matplotlib
Microcontroller software
  ARM Cortex-M4 microcontroller drives the system
  Hardware interfaces with the PC over USB

## Slide 6: Design — Signal Generation
Frequency range: 1 kHz to 150 MHz
Analog Devices AD9958: dual 500 MSPS sine wave synthesizer
  fs/2 = 250 MHz
  no lower limit

## Slide 7: Design — Signal Output
Two-stage output amplifier: RF op amps
  Synthesizer outputs -8.5 dBm
  Each stage 15.5 dB: 22.5 dBm maximum
    Margin!
Amplitude range: up to 1.25 V RMS or 15 dBm

## Slide 8: Design — Phase Detection
Tests phase response
Second synthesizer output (this is the phase reference) is combined with input signal
Sweep phase to find the null

## Slide 9: Design — Detection
Low-noise frontend:
  Wideband buffer isolates input from…:
  Power combiner: sum in the phase reference
  AD8310 logarithmic amplifier: 95 dB range
  RF shield: blocks radio interference
Must detect signals down to 60 dB

## Slide 10: Schedule
Item | Start Date | End Date | Percent Complete
PRS | 2014-10-03 | 2014-10-17 | 100%
PDP | 2014-10-17 | 2014-10-31 | 100%
Architecture Presentation | 2014-10-31 | 2014-11-14 | 100%
Interim Report | 2014-11-14 | 2014-12-05 | 100%
Proto. built | 2014-11-14 | 2014-12-05 | 100%
Proto. firmware | 2014-11-10 | 2014-12-05 | 100%

## Slide 11: Budget
Item | Expended | Actual | Est. to Completion | Est. at Completion
Synthesizer | $60 | $60 | $0 | $60
Input | $70 | $70 | $0 | $70
Output amp. | $66 | $66 | $0 | $66
Power supply | $0 | $0 | $0 | $0
Final build | $0 |  | $120 | $120
Enclosure | $0 |  | $30 | $30
Misc/re-spins | $0 |  | $100 | $100
Total | $196 | $196 | $250 | $446

## Slide 12: Next Steps
Hardware
Combine prototypes into a final product
Software
Finish firmware with full analysis capability
Write PC software that receives and plots data

## Slide 13: Conclusion
Product can capture Bode plots
Uses signal synthesizer, output amplifier, input frontend, ADC, and microcontroller
These have been prototyped and tested